## Slide 1: ECE1004 – Signals and Systems
Dr. Florence Gnana Poovathy J
Assistant Professor (Senior)
School of Electronics Engineering (SENSE)
VIT-Chennai
Fall 2022-2023 Semester
VIT-Chennai - SENSE

## Slide 2: Suggested Readings
Alan. V. Oppenheim, Alan. S. Willsk, S. Hamid Nawab, “Signals and Systems”, 2013, second edition, Pearson Education Limited, Noida, India.
VIT-Chennai - SENSE

## Slide 3
An Overview of ‘Signals and Systems’
Figure 1:A typical example
VIT-Chennai - SENSE

## Slide 4
Contents
1
Module 1: Introduction to Continuous Time and Discrete Time Signals
VIT-Chennai - SENSE

## Slide 5: Module 1: Introduction to Signals
Topics to be covered in Module 1
Representation of Signals
Classification of Signals/Types of signals Operations on Signals
VIT-Chennai - SENSE

## Slide 7: Module 1: Introduction to Signals
Signal Representation
A continuous-time signal x (t) can be represented in functional and graphical forms.
A discrete-time signal x [n] can be represented in tabular, functional, graphical and sequential forms.
A deterministic x (t) or x [n] can be expressed/represented in terms of step and ramp functions (as shown in Figure 23).
Figure 23:Signal representation - example
VIT-Chennai - SENSE

## Slide 8: Module 1: Introduction to Signals
Classification of Signals
Continuous-time signal versus discrete-time signal Continuous-value signal versus discrete-valuesignal
Deterministic signal versus random signal
Even signal versus odd signal Periodic signal versus aperiodic signal Energy signal versus power signal
VIT-Chennai - SENSE

## Slide 9: Module 1: Introduction to Signals
Continuous-time signal versus discrete-time signal
Continuous Time (CT) Signal: A signal x (t) that is specified for all value of time t
Discrete Time (DT) Signal: A signal y [n] that is specified only for integer value of n
Figure 2:Continuous-time versus discrete-time signal
VIT-Chennai - SENSE

## Slide 10
Module 1: Introduction to Signals
Example 1.1: Sketch the waveforms of the CT signal x (t) = t and DT signal x [n] = n
Figure 3:Waveforms of CT and DT signals
VIT-Chennai - SENSE

## Slide 11: Module 1: Introduction to Signals
Continuous-value signal versus discrete-value signal
Continuous-Value Signal: A signal x (t) whose amplitude can take on any value
Discrete-Value Signal: A signal y (t) whose amplitude can take on only a finite number of values
Figure 4:Continuous-value versus discrete-value signal
VIT-Chennai - SENSE

## Slide 12: Module 1: Introduction to Signals
Deterministic signal versus randon signal
Deterministic Signal: A signal x (t) that can be mathematically modeled explicitly as a function of time, i.e., x (t) = A sin(2πf0t)
Random Signal: A signal y (t) that is known only in terms of probabilistic description, i.e., noise
Figure 5:Deterministic versus random signal
VIT-Chennai - SENSE

## Slide 13: Module 1: Introduction to Signals
Even signal versus odd signal
Even Signal: A signal xe (t) that satisfies the condition xe (t) = xe (−t)
Odd Signal: A signal xo (t) that satisfies the condition
xo (t) = −xo (−t)
Figure 6:Even versus odd signal
VIT-Chennai - SENSE

## Slide 14: Module 1: Introduction to Signals
Any deterministic signal x (t) can be expressed as a sum of an even signal and an odd signal: x (t) = xe (t) + xo (t) where
e
1
2
x (t) = x (t) + x (−t)
, ,
o
1
2
and x (t) = x (t) −
, ,
x (−t) (1)
Example 1.2: Show that x (t) = A sin(2πf0t) is an odd signal
Given x (t) = A sin(2πf0t) Therefore, x (−t) = A sin(2πf0 × (−t))
= A × , − sin(2πf0t), since sin(−θ) = − sin(θ)
= −A sin(2πf0t)
x (−t) = −x (t)
Hence, x (t) is an odd signal
VIT-Chennai - SENSE

## Slide 15: Module 1: Introduction to Signals
Example 1.3: Find the even and odd components of the signal
x (t) = cos(t) + sin(t) cos(t)
The even component,
e
1
2
,
x (t) = x (t) + x (−t)
,
1
2
,
= cos(t) + sin(t) cos(t) + cos(
−t) + sin(−t) cos(−t)
,
1
2
,
= cos(t) + sin(t) cos(t) + cos(t) − sin(t) cos(t)
,
= cos(t)
Note:sin( −θ) = − sin(θ) and cos(−θ) = cos(θ)
VIT-Chennai - SENSE

## Slide 16: Module 1: Introduction to Signals
The odd component,
o
1
2
,
x (t) = x (t) − x (−t)
,
1
2
,
= cos(t) + sin(t) cos(t) − cos(−t) − sin(−t) cos(
−t)
,
1
2
= cos(t) + sin(t) cos(t)− cos(t) + sin(t) cos(t)
, ,
= sin(t) cos(t)
VIT-Chennai - SENSE

## Slide 17: Module 1: Introduction to Signals
Characteristics/properties of Even and Odd Signals
For an even signal,
∫
T
0
−T0
∫
T
0
0
xe (t)dt = 2 xe (t)dt
For an odd signal,
∫
T
0
xo (t)dt = 0
−T0
The product of two even signals is an even signal The product of two odd signals is an even signal
The product of an even signal and an odd signal is an odd signal
VIT-Chennai - SENSE

## Slide 18: Module 1: Introduction to Signals
Periodic signal versus aperiodic signal
Periodic Signal: A continuous-time signal x (t) with a constant period 0 < T0 < ∞ such that
x (t) = x (t + T0) (2)
(or) a discrete-time signal x [n] with a constant integer period 0 < K0 < ∞ such that
x [n] = x [n + K0]
(3)
Aperiodic Signal: A signal y (t) or y [n] that does not satisfy the above property
VIT-Chennai - SENSE

## Slide 19
Module 1: Introduction to Signals
Figure 7:Periodic versus aperiodic signals
VIT-Chennai - SENSE

## Slide 20: Module 1: Introduction to Signals
Energy-type signal versus power-type signal
Energy-type signal: A signal x (t) or x [n] that has a finite energy Ex
such that 0 < Ex < ∞ where
x
∫
∞
−∞
2
E = |x (t)| dt
in the case of CT signal (4)
or
∞
Σ
2
Ex = |x [n]| dt in the case of DT signal
n=−∞
Note that the power of an energy-type signal will be zero.
(5)
VIT-Chennai - SENSE

## Slide 21: Module 1: Introduction to Signals
Power-type signal: A signal x (t) or x [n] that has a finite power Px
such that 0 < Px < ∞ where
x
P = lim
1
T→∞ T
∫ T
−
T
2
2
|x (t)| dt in the case of CT signal (6)
or
x
P = lim
1
K→∞ 2K + 1 n=−K
K
Σ
|x [n]|
2
in the case of DT signal (7)
Note that the energy of a power-type signal will be infinity.
VIT-Chennai - SENSE
Winter 2021-2022 Semester 19 / 50

## Slide 22: Module 1: Introduction to Signals
In the case of a periodic signal, i.e. x (t) with a period T0 or x [n] with a period K0
1
Px = T
0 t1
∫
t +T
1 0
2
|x (t)| dt in the case of CT signal (8)
or
x
1
P =
K0
k+K0−1
Σ
n=k
|x [n]|
2
in the case of DT signal.
(9)
In general, power-type signals are periodic but NOT all periodic signals are of power-type.
VIT-Chennai - SENSE

## Slide 23
Figure 8:Energy signal versus power signal
VIT-Chennai - SENSE

## Slide 24: Module 1: Introduction to Signals
Example 1.4: Determine the energy and power of the signal
x (t) = A cos(2πf0t).
x
Energy of x(t): E =
∞
−∞
∫
∫
2
|x (t)| dt
=
∞
−∞
0
2
|A cos(2πf t)| dt = ∞
.
Power of x(t):
x
P = lim
1
T→∞ T
∫ T
−
T
2
2
|x (t)| dt
= lim
1
T→∞ T
∫ T
−
T
2
0
2
A2
2
|A cos(2πf t)| dt = .
Hence, x (t) is a power-type signal.
VIT-Chennai - SENSE

## Slide 25: Module 1: Introduction to Signals
Example 1.5: Determine the energy and power of y (t) = exp(−|t|).
y
∫
∞
−∞
2
Energy of y(t): E = |y (t)| dt
∫
∞
−∞
= | exp(−|
2
t|)| dt
∫
∞
0
2
= 2 | exp(−t)| dt
modulus removal
∫
∞
0
1
2
= 2 exp(−2t)dt = 2 × = 1.
Power of y(t):
y
P = lim
1
T→∞ T
∫
−
T
2
2
|y (t)| dt
1
= lim × {a finite value} = 0.
T→∞ T
Hence, x (t) is an energy-type signal.
VIT-Chennai - SENSE

## Slide 26: Module 1: Introduction to Signals
Elementary signals Exponential signal Sinusoidal signal
Complex-exponential signal
Singularity functions/signals
Impulse function Step function Ramp function Signum function
Rectangular function Sinc function
VIT-Chennai - SENSE

## Slide 27: Module 1: Introduction to Signals
Exponential signal: x (t) = A exp(at) where 0 < |a| < ∞ is a non-zero parameter/constant.
For a > 0, x (t) is growing For a < 0, x (t) is decaying
Figure 9:Exponential signals
VIT-Chennai - SENSE

## Slide 28
Module 1: Introduction to Signals
Sinusoidal signal: x (t) = A cos(2πf0t + θ) or x (t) = A sin(2πf0t + θ) where A is the amplitude, f0 is the frequency (in Hertz) and θ is the phase angle (in radian).
Figure 10:A CT sinusoidal signal with period T0 = 1
f0
VIT-Chennai - SENSE

## Slide 29: Module 1: Introduction to Signals
Complex exponential signal:
x (t) = A exp(j 2πf0t) = A cos(2πf0t) + j A sin(2πf0t) where A is the magnitude and f0 is the frequency. Note that the power of x (t) is A2.
Figure 11:A complex exponential signal x (t) = A exp(j 2πf0t) where A = 3 and
f0 = 1/π (source video:Click here and watch from 7:10 to 7:30 sec)
VIT-Chennai - SENSE

## Slide 30: Module 1: Introduction to Signals
Unit impulse function in CT (dirac delta): A function δ(t) defined as
δ(t) =
.
1, t = 0
0, elsewhere
Figure 12:CT impulse functions
VIT-Chennai - SENSE

## Slide 31: Module 1: Introduction to Signals
Unit impulse function in DT (dirac delta): A function δ[n] defined as
δ[n] =
.
1, n = 0
0, n ̸= 0
Figure 13:DT impulse functions
VIT-Chennai - SENSE

## Slide 32: Module 1: Introduction to Signals
Unit step function in CT: A function u(t) defined as
u(t) =
.
1, t ≥ 0
0, t < 0
Figure 14:CT unit step function
VIT-Chennai - SENSE

## Slide 33: Module 1: Introduction to Signals
Unit step function in DT: A function u[n] defined as
.
u[n] =
1, n ≥ 0
0, n < 0
Figure 15:DT unit step function
VIT-Chennai - SENSE

## Slide 34: Module 1: Introduction to Signals
Unit ramp function in CT: A function r (t) defined as
r (t) =
.
t, t ≥ 0
0, t < 0
Figure 16:CT unit ramp function
VIT-Chennai - SENSE
Winter 2021-2022 Semester 32 / 50

## Slide 35: Module 1: Introduction to Signals
Unit ramp function in DT: A function r [n] defined as
r [n] =
.
n, n ≥ 0
0, n < 0
Figure 17:DT unit ramp function
VIT-Chennai - SENSE

## Slide 36: Module 1: Introduction to Signals
Signum function in CT: A function sgn(t) defined as

sgn(t) =

1, t > 0
−1, t < 0
0, t = 0
Figure 18:CT signum function
VIT-Chennai - SENSE

## Slide 37: Module 1: Introduction to Signals
Signum function in DT (dirac delta): A function sgn[n] defined as

sgn[n] =

1, n > 0
−1, n < 0
0, n = 0
Figure 19:DT unit step function
VIT-Chennai - SENSE

## Slide 38: Module 1: Introduction to Signals
Unit rectangular function in CT: A function rect
t
T
defined as
rect
t
T
=
.
1, |t| ≤ T/2 0, otherwise
Figure 20:CT unit rectangular function
VIT-Chennai - SENSE

## Slide 39: Module 1: Introduction to Signals
n
K
Unit rectangular function in DT: A function rect ( ) defined as
n
K
Rect( ) =
.
1, |n| ≤ ⌊K/2⌋
0, otherwise
Figure 21:DT unit rectangular function
VIT-Chennai - SENSE

## Slide 40: Module 1: Introduction to Signals
Sinc function: The sinc function is defined as sinc(t) = sin(πt)
πt
Figure 22:Sinc functions
s
Note that x (t) =
Σ
∞
n=−∞
s s s
1
Fs
s
x (nT ) × δ(t − nT ) where T = (T is the
sampling interval and Fs is the sampling frequency).
VIT-Chennai - SENSE
Winter 2021-2022 Semester 38 / 50

## Slide 41: Module 1: Introduction to Signals
Operations on Signals Amplitude scaling Time shifting
Time scaling
VIT-Chennai - SENSE

## Slide 42
Module 1: Introduction to Signals
Amplitude scaling: The operation Ax (t) or Ax [n] is to multiply the amplitude of x (t) (or x[n]) by an amount A
Figure 24:Amplitude scaling
VIT-Chennai - SENSE

## Slide 43
Module 1: Introduction to Signals
Time shifting: The operation x (t − T ) or x [n − K ] is to shift x (t) (or x[n]) by an amount T (or K )
Figure 25:Time shifting
VIT-Chennai - SENSE

## Slide 44
Module 1: Introduction to Signals
Example 1.6: Sketch the waveform x (t) = 2u(t) − u(t − 2)
Figure 26:Answer to example 1.6
VIT-Chennai - SENSE

## Slide 45
Module 1: Introduction to Signals
Figure 27:Answer to example 1.6 - continued
VIT-Chennai - SENSE

## Slide 46: Module 1: Introduction to Signals
Time scaling in CT: The operation x (at) is to scale the time-axis of x (t) by a constant a
a > 1 contracts/shrinks the function horizontally
2 3
A proper fraction 0 < a < 1 (for example: 1 and 1 ) expands the
function horizontally
a < 0 leads to time inversion or time reversal
Figure 28:CT Time Scaling
VIT-Chennai - SENSE

## Slide 47: Module 1: Introduction to Signals
Time scaling in DT: The operation x [Kn] is to scale the discrete time-axis of x [n] by a integer K
K > 1 contracts/shrinks the function horizontally
2 3
A proper fraction 0 < K < 1 (for example: 1 and 1 ) expands the
function horizontally
K < 0 leads to time inversion or time reversal
Figure 29:DT Time Scaling
VIT-Chennai - SENSE
Winter 2021-2022 Semester 46 / 50

## Slide 48: Module 1: Introduction to Signals
y (t) = −2 x ((t-3)/2)
Example 1.7: If the waveform x (t) is as shown in Figure 30, sketch the waveform
(Hint: Time scaling → time shifting → amplitude scaling)
Figure 30:The waveform x (t) for example 1.7
VIT-Chennai - SENSE

## Slide 49
Module 1: Introduction to Signals
Figure 31:Answer to example 1.7
VIT-Chennai - SENSE

## Slide 50
Module 1: Introduction to Signals
Figure 32:Answer to example 1.7 - continued
VIT-Chennai - SENSE

## Slide 51: Module 1: Introduction to Signals
Module 1 - Summary
Classification of signals: continuous-time or discrete-time,
continuous-valued or discrete-valued, random or deterministic, even or odd, periodic or aperiodic and energy or power
Elementary signals (sinusoidal, exponential, complex-exponential, etc.) and singularity signals (unit impulse, unit step, unit ramp, etc.)
Signal representation: tabular, functional, graphical and sequential forms
Operations on signals: amplitude scaling, time shifting and time scaling
VIT-Chennai - SENSE